Execution Performance Tester
Documentation
Version: 0

Specification and requirements

The scope of this module to be able to precisely measure the context switching overheads in a system.

  1. NIOSii Economy core based
  2. No CPU caching (neither data and instruction)
  3. No branch prediction support
  4. Non-vectored interrupt handling
  5. The core is able to detect task execution switches
  6. No Multitasking support
  7. Scaleable via parameters (124 different tasks / M4K block RAM)
  8. Measures exception handling timings such as: interrupt latency, context saving, interrupt service routin, context restoring
2. The Hardware Core
  1. Conceptual block diagram - it consists of 3 different parts
    1. On-chip RAM: stores the actual measurement data (Task IDs: words-4, exception timings: 4)
    2. Controller: detecting task and context switchings, putting timestamps, organizing data in the memory
    3. Timestamp counter (the instance is in the controller module)
      Consider 40 bit counter @ 50 MHz → (240-1)*20ns = 21990.233 sec total execution time (from measurement start to stop → total time).

  1. Using a single M4K(128x32) on-chip memory block (Cyclone II) enables to measure only 124 different tasks because the last 4 words is reserved for the exception timings. The maximum duration at 50MHz for each task and exception parameters is (240-1)*20ns = 85.9 sec, but currently no overflow prevention is implemented.
  2. Test and function
2. Memory Mapping
3. Software Stack Architecture
4. Functionality Tests
5. I/O Offset Calibration
6. Scheduler Implementation